## Slide 1: Networking Fundamentals
Foundations of Ethernet and IP

## Slide 2: IPv4 Addressing
IPv4 addressing and binary conversion
#

## Slide 3: Binary Counting
Each position from right to left is an increased power of 2
  The right-most position is 20, the next left position is 21, etc.
Add together all positions which are a 1 to convert the binary number to decimal
1 0 1 0 1 1 0 0
27
26
25
24
23
22
21
20
128 + 0 + 32 + 0 + 8 + 4 + 0 + 0 = 172
128 64 32 16 8 4 2 1

## Slide 4: IPv4 Address
32 bit address field
4 Octets
00000000.00000000.00000000.00000000
|-8 bits|
|------------32 bits---------------|
11111111.11111111.11111111.00000000
|-hosts-|
|---------24 bits---------|
|----------network--------|
Example 24-bit mask
Comprised of a network identifier and host identifier
Definition of host and network portion is defined by a mask
  1s indicate network portion, 0s indicate host portion

## Slide 5: Subnet Masks
Can be expressed in dotted decimal or CIDR (/24)
Often referred to as a prefix length
11111111.11111111.11111000.00000000
10101100.00010000.00001010.00000101
10101100.00010000.00001000.00000000
11111111.11111111.11111111.00000000
|-hosts-|
|---------24 bits---------|
|---------network---------|
|---hosts--|
|-------21 bits--------|
|------- network-------|
11111111.11111111.11111000.00000000
172.16.10.5/21
172.16.8.0/21
IP Address
Mask
Network ID

## Slide 6: RFC1918 Address Spaces
Private addresses are not routable on the internet
  They do not uniquely identify a device on the internet
3 private address spaces:
10.0.0.0/8
  A single Class A network
172.16.0.0/12
  16 contiguous Class B networks
192.168.0.0/16
  256 contiguous Class C networks
Class A - /8
Class B - /16
Class C - /24