## Slide 1: Networking Fundamentals
Foundations of Ethernet and IP

## Slide 2: IPv6 Concepts
Working with a 128-bit address
#

## Slide 3: IPv6 Address Overview
128-bit address field
8 hextets, separated by colons
Subnet mask works exactly like IPv4, just longer
Address compression rules:
  Remove all preceding 0s in a hextet
  *Replace contiguous hextets of 0s with double colon ::
  *Once per address
2001:0DB8:0000:0000:0000:0123:4567:89AB
|16 bits|
|---------------128 bits---------------|
2001:DB8::123:4567:89AB
2001:0DB8:0000:0000:0000:0123:4567:89AB

## Slide 4: IPv6 Address Types
Global Unicast
  2000::/3 – analogous to IPv4 public address space
Unique Local
  fc00::/7 – analogous to RFC1918 IPV4 private address space
Link Local
  fe80::/64 – not routable
Anycast
  Same as global unicast but belonging to multiple nodes
Multicast
  ff00::/8
Modified EUI 64
  Process used to self assign a globally unique IPv6 address
Most common prefix length is /64
  /64 is even recommended on point-to-point links due to EUI-64 compatibility

## Slide 5: Anycast vs. Multicast
Multicast = 1 to many
Anycast = 1 to closest
Anycast uses same addresses as Global Unicast
Well-known multicast addresses:
  ff02::1 - All IPv6 devices (broadcast)
  ff02::2 - All IPv6 routers
  ff02::5 - All OSPFv3 routers
  ff02::a - All EIGRP(IPv6) routers